IX configuration guide – Arista

Global Config
no ip multicast-routing

VLAN Config
vlan 300
   name IX_NAME

1. Interface Config (
  1. As Intermediate Switch
interface ethernetY
description IX_NAME
  switchport access vlan 300
  arp timeout 7200
  ipv6 enable
  ipv6 nd ra suppress all
  no lldp transmit
  no ntp serve
  spanning-tree bpdufilter enable

  1. As Router
interface ethernetY
no switchport
description IX_NAME
ipv6 enable
  ipv6 nd ra suppress all
  no lldp transmit
  no ntp serve
ip address x.x.x.x y.y.y.y
ipv6 address x::y/64
arp timeout 7200
no lldp transmit
no ip pim

1. Basic BGP Config
  1. prefix-lists
ip prefix-list BOGONSIPv4 seq 10 deny 0.0.0.0/8 le 32
ip prefix-list BOGONSIPv4 seq 20 deny 10.0.0.0/8 le 32
ip prefix-list BOGONSIPv4 seq 30 deny 100.64.0.0/10 le 32
ip prefix-list BOGONSIPv4 seq 40 deny 127.0.0.0/8 le 32
ip prefix-list BOGONSIPv4 seq 50 deny 169.254.0.0/16 le 32
ip prefix-list BOGONSIPv4 seq 60 deny 172.16.0.0/12 le 32
ip prefix-list BOGONSIPv4 seq 70 deny 192.0.0.0/24 le 32
ip prefix-list BOGONSIPv4 seq 80 deny 192.0.2.0/24 le 32
ip prefix-list BOGONSIPv4 seq 90 deny 192.168.0.0/16 le 32
ip prefix-list BOGONSIPv4 seq 100 deny 198.18.0.0/15 le 32
ip prefix-list BOGONSIPv4 seq 110 deny 198.51.100.0/24 le 32
ip prefix-list BOGONSIPv4 seq 120 deny 203.0.113.0/24 le 32
ip prefix-list BOGONSIPv4 seq 130 deny 224.0.0.0/3 le 32
ip prefix-list BOGONSIPv4 seq 9999 permit 0.0.0.0/0 le 24

ipv6 prefix-list BOGONSIPv6 deny 3ffe::/16 le 128
ipv6 prefix-list BOGONSIPv6 deny 2001:db8::/32 le 128
ipv6 prefix-list BOGONSIPv6 permit 2001::/32
ipv6 prefix-list BOGONSIPv6 deny 2001::/32 le 128
ipv6 prefix-list BOGONSIPv6 permit 2002::/16
ipv6 prefix-list BOGONSIPv6 deny 2002::/16 le 128
ipv6 prefix-list BOGONSIPv6 deny 0000::/8 le 128
ipv6 prefix-list BOGONSIPv6 deny fe00::/9 le 128
ipv6 prefix-list BOGONSIPv6 deny ff00::/8 le 128
ipv6 prefix-list BOGONSIPv6 permit 2000::/3 le 48
ipv6 prefix-list BOGONSIPv6 deny 0::/0 le 128

ip prefix-list MY_V4_PREFIXES seq 10 permit x.x.x.x/y eq/le/ge n
ip prefix-list DOWNSTREAM_V4_PREFIXES seq 10 permit x.x.x.x/y eq/le/ge n

ipv6 prefix-list MY_V6_PREFIXES permit x::/y eq/le/ge n
ipv6 prefix-list DOWNSTREAM_V6_PREFIXES permit x::/y eq/le/ge n
  1. route-maps
route-map EBGP_V4_OUT permit 10
 match ip address prefix-list MY_V4_PREFIXES
 set community A:N
route-map EBGP_V4_OUT permit 20
 match ip address prefix-list DOWNSTREAM_V4_PREFIXES
 set community A:N

route-map EBGP_V6_OUT permit 10
match ipv6 address prefix-list MY_V6_PREFIXES
set community A:N
route-map EBGP_V6_OUT permit 20
match ipv6 address prefix-list DOWNSTREAM_V6_PREFIXES
set community A:N

route-map IX_NAME_V4_IN deny 10
match ip address prefix-list BOGONSIPv4

route-map IX_NAME_V4_IN permit 20
set local-preference {YOUR_LOCAL_PREF}
set community A:N

route-map IX_NAME_V6_IN deny 10
match ip address prefix-list BOGONSIPv6

route-map IX_NAME_V6_IN permit 20
set local-preference {YOUR_LOCAL_PREF}
set community A:N

~
  1. router bgp
router-id x.x.x.x
network x.x.x.x/y
neighbor IX_NAME_V4 peer-group
neighbor IX_NAME_V4 remove-private-as all
neighbor IX_NAME_V4 local-v4-addr 196.10.140.39
neighbor IX_NAME_V4 route-map IX_NAME_V4_IN in
neighbor IX_NAME_V4 route-map IX_NAME_V4_OUT out
neighbor IX_NAME_V4 send-community
neighbor IX_NAME_V4 maximum-routes 12000
neighbor IX_NAME_V4 graceful-restart
neighbor IX_NAME_V4 soft-reconfiguration inbound all

neighbor IX_NAME_V6 peer-group
neighbor IX_NAME_V6 remove-private-as all
neighbor IX_NAME_V6 route-map IX_NAME_V6_IN in
neighbor IX_NAME_V6 route-map IX_NAME_V6_OUT out
neighbor IX_NAME_V6 send-community
neighbor IX_NAME_V6 maximum-routes 12000
neighbor IX_NAME_V6 graceful-restart
neighbor IX_NAME_V6 soft-reconfiguration inbound all

neigh x.x.x.y peer-group IX_NAME_V4
neigh x.x.x.y remote-as {PEER_ASN}
neigh x.x.x.y description DESCRIPTION

neigh x::y peer-group IX_NAME_V6
neigh x::y remote-as {PEER_ASN}
neigh x::y description IX_NAME_ROUTE_SERVER
no neighbor x::y enforce-first-as

address-family ipv4
neighbor IX_NAME_V4 activate
  !
address-family ipv6
neighbor IX_NAME_V6 activate