set interfaces ae3 description "IX_NAME”
set interfaces ae3 mtu 9192
set interfaces ae3 aggregated-ether-options minimum-links 1
set interfaces ae3 aggregated-ether-options link-speed 10g
set interfaces ae3 aggregated-ether-options lacp active
set interfaces ae3 aggregated-ether-options lacp periodic fast
set interfaces ae3 aggregated-ether-options lacp link-protection disable
set interfaces ae3 aggregated-ether-options lacp link-protection revertive

set interfaces xe-x/x/x description "IX_NAME_AE3”
set interfaces xe-x/x/x gigether-options 802.3ad ae3
set interfaces xe-x/x/y description "IX_NAME_AE3”
set interfaces xe-x/x/y gigether-options 802.3ad ae3

set interfaces ae3 unit 0 bandwidth 20g
set interfaces ae3 unit 0 family inet sampling input
set interfaces ae3 unit 0 family inet sampling output
set interfaces ae3 unit 0 family inet address x.x.x.x/y
set interfaces ae3 unit 0 family inet no-redirects
set interfaces ae3 unit 0 family inet6 address x::y/64
OR
set interfaces xe-x/y/z unit 0 description "IX_NAME"
set interfaces xe-x/y/z unit 0 bandwidth 10g
set interfaces xe-x/y/z unit 0 family inet sampling input
set interfaces xe-x/y/z unit 0 family inet sampling output
set interfaces xe-x/y/z unit 0 family inet address x.x.x.x/y
set interfaces xe-x/y/z unit 0 family inet no-redirects
set interfaces xe-x/y/z unit 0 family inet6 address x::y/64

set protocols bgp group IX_NAME_LG type external
set protocols bgp group IX_NAME_LG neighbor x.x.x.1 description IX_NAME_LG
set protocols bgp group IX_NAME_LG peer-as {COLLECTOR_AS}
set protocols bgp group IX_NAME_LG neighbor x.x.x.1 local-address x.x.x.x
set protocols bgp group IX_NAME_LG neighbor x.x.x.1 import ROUTE_COLLECTOR_IN
set protocols bgp group IX_NAME_LG neighbor x.x.x.1 export EBGP-EXPORT-TJB
set protocols bgp group IX_NAME_LG neighbor x.x.x.1 remove-private
set protocols bgp group IX_NAME_RS type external
set protocols bgp group IX_NAME_RS peer-as {ROUTE_SERVER_AS}
set protocols bgp group IX_NAME_RS neighbor x.x.x.2 description IX_NAME_RS1
set protocols bgp group IX_NAME_RS neighbor x.x.x.2 local-address x.x.x.x
set protocols bgp group IX_NAME_RS neighbor x.x.x.2 import [ REJECT-BOGONMARTIAN IX_NAME_RS_IN ]
set protocols bgp group IX_NAME_RS neighbor x.x.x.2 family inet unicast prefix-limit maximum 100000
set protocols bgp group IX_NAME_RS neighbor x.x.x.2 export EBGP-EXPORT-TJB
set protocols bgp group IX_NAME_RS neighbor x.x.x.2 remove-private
set protocols bgp group IX_NAME_RS neighbor x.x.x.3 description IX_NAME_RS2
set protocols bgp group IX_NAME_RS neighbor x.x.x.3 local-address x.x.x.x
set protocols bgp group IX_NAME_RS neighbor x.x.x.3 import [ REJECT-BOGONMARTIAN IX_NAME_RS_IN ]
set protocols bgp group IX_NAME_RS neighbor x.x.x.3 family inet unicast prefix-limit maximum 100000
set protocols bgp group IX_NAME_RS neighbor x.x.x.3 export EBGP-EXPORT-TJB
set protocols bgp group IX_NAME_RS neighbor x.x.x.3 remove-private

set protocols bgp group IX_NAME_V6 type external
set protocols bgp group IX_NAME_V6 local-address x::y
set protocols bgp group IX_NAME_V6 export IX_NAME_v6_OUT
set protocols bgp group IX_NAME_V6 neighbor x::1 description IX_NAME_LG-v6
set protocols bgp group IX_NAME_V6 neighbor x::1 import ROUTE_COLLECTOR_IN
set protocols bgp group IX_NAME_V6 neighbor x::1 remove-private
set protocols bgp group IX_NAME_V6 neighbor x::1 peer-as {COLLECTOR_AS}
set protocols bgp group IX_NAME_V6 neighbor x::2 description IX_NAME_RS1_v6
set protocols bgp group IX_NAME_V6 neighbor x::2 import [ REJECT-BOGONMARTIAN IX_NAME_v6_IN ]
set protocols bgp group IX_NAME_V6 neighbor x::2 remove-private
set protocols bgp group IX_NAME_V6 neighbor x::2 peer-as {ROUTE_SERVER_AS}
set protocols bgp group IX_NAME_V6 neighbor x::3 description IX_NAME_RS2_v6
set protocols bgp group IX_NAME_V6 neighbor x::3 import [ REJECT-BOGONMARTIAN IX_NAME_v6_IN ]
set protocols bgp group IX_NAME_V6 neighbor x::3 remove-private
set protocols bgp group IX_NAME_V6 neighbor x::3 peer-as {ROUTE_SERVER_AS}

set policy-options policy-statement IX_NAME_v6_OUT term SELF from family inet6
set policy-options policy-statement IX_NAME_v6_OUT term SELF from protocol aggregate
set policy-options policy-statement IX_NAME_v6_OUT term SELF from route-filter {MY_PREFIXES} exact
set policy-options policy-statement IX_NAME_v6_OUT term SELF then accept
set policy-options policy-statement IX_NAME_v6_OUT term TRANSIT from family inet6
set policy-options policy-statement IX_NAME_v6_OUT term TRANSIT from community transit-cust-with-own-routes
set policy-options policy-statement IX_NAME_v6_OUT term TRANSIT from route-filter ::0/0 upto /48
set policy-options policy-statement IX_NAME_v6_OUT term TRANSIT then accept
set policy-options policy-statement IX_NAME_v6_OUT term REJECT-ALL-ELSE then reject

set policy-options policy-statement IX_NAME_v6_IN term RECEIVE-ALL from protocol bgp
set policy-options policy-statement IX_NAME_v6_IN term RECEIVE-ALL then community set ix-tjb
set policy-options policy-statement IX_NAME_v6_IN term RECEIVE-ALL then community add ix_peer
set policy-options policy-statement IX_NAME_v6_IN term RECEIVE-ALL then accept

set policy-options policy-statement REJECT-BOGONMARTIAN term OWN_PREFIXES from route-filter {MY_PREFIXES} orlonger
set policy-options policy-statement REJECT-BOGONMARTIAN term OWN_PREFIXES from route-filter {MY_PREFIXES} orlonger
set policy-options policy-statement REJECT-BOGONMARTIAN term OWN_PREFIXES then reject
set policy-options policy-statement REJECT-BOGONMARTIAN term v4_MARTIANS from family inet
set policy-options policy-statement REJECT-BOGONMARTIAN term v4_MARTIANS from route-filter 0.0.0.0/0 exact
set policy-options policy-statement REJECT-BOGONMARTIAN term v4_MARTIANS from route-filter 0.0.0.0/8 orlonger
set policy-options policy-statement REJECT-BOGONMARTIAN term v4_MARTIANS from route-filter 10.0.0.0/8 orlonger
set policy-options policy-statement REJECT-BOGONMARTIAN term v4_MARTIANS from route-filter 100.64.0.0/10 orlonger
set policy-options policy-statement REJECT-BOGONMARTIAN term v4_MARTIANS from route-filter 127.0.0.0/8 orlonger
set policy-options policy-statement REJECT-BOGONMARTIAN term v4_MARTIANS from route-filter 169.254.0.0/16 orlonger
set policy-options policy-statement REJECT-BOGONMARTIAN term v4_MARTIANS from route-filter 172.16.0.0/12 orlonger
set policy-options policy-statement REJECT-BOGONMARTIAN term v4_MARTIANS from route-filter 192.0.0.0/24 orlonger
set policy-options policy-statement REJECT-BOGONMARTIAN term v4_MARTIANS from route-filter 192.0.2.0/24 orlonger
set policy-options policy-statement REJECT-BOGONMARTIAN term v4_MARTIANS from route-filter 192.88.99.0/24 orlonger
set policy-options policy-statement REJECT-BOGONMARTIAN term v4_MARTIANS from route-filter 192.168.0.0/16 orlonger
set policy-options policy-statement REJECT-BOGONMARTIAN term v4_MARTIANS from route-filter 198.18.0.0/15 orlonger
set policy-options policy-statement REJECT-BOGONMARTIAN term v4_MARTIANS from route-filter 198.51.100.0/24 orlonger
set policy-options policy-statement REJECT-BOGONMARTIAN term v4_MARTIANS from route-filter 203.0.113.0/24 orlonger
set policy-options policy-statement REJECT-BOGONMARTIAN term v4_MARTIANS from route-filter 224.0.0.0/4 orlonger
set policy-options policy-statement REJECT-BOGONMARTIAN term v4_MARTIANS then reject
set policy-options policy-statement REJECT-BOGONMARTIAN term v6_MARTIANS from family inet6
set policy-options policy-statement REJECT-BOGONMARTIAN term v6_MARTIANS from route-filter 3ffe::/16 orlonger
set policy-options policy-statement REJECT-BOGONMARTIAN term v6_MARTIANS from route-filter 0000::/8 orlonger
set policy-options policy-statement REJECT-BOGONMARTIAN term v6_MARTIANS from route-filter 2001:db8::/32 orlonger
set policy-options policy-statement REJECT-BOGONMARTIAN term v6_MARTIANS from route-filter 2001::/32 exact next policy
set policy-options policy-statement REJECT-BOGONMARTIAN term v6_MARTIANS from route-filter 2001::/32 longer
set policy-options policy-statement REJECT-BOGONMARTIAN term v6_MARTIANS from route-filter 2002::/16 exact next policy
set policy-options policy-statement REJECT-BOGONMARTIAN term v6_MARTIANS from route-filter 2002::/16 longer
set policy-options policy-statement REJECT-BOGONMARTIAN term v6_MARTIANS from route-filter fe00::/9 orlonger
set policy-options policy-statement REJECT-BOGONMARTIAN term v6_MARTIANS from route-filter ff00::/8 orlonger
set policy-options policy-statement REJECT-BOGONMARTIAN term v6_MARTIANS from route-filter 2000::/3 prefix-length-range /49-/128
set policy-options policy-statement REJECT-BOGONMARTIAN term v6_MARTIANS from route-filter 0::/0 orlonger
set policy-options policy-statement REJECT-BOGONMARTIAN term v6_MARTIANS then reject
set policy-options policy-statement REJECT-BOGONMARTIAN then next policy

set policy-options policy-statement IX_NAME_RS_IN term RECEIVE-ALL from protocol bgp
set policy-options policy-statement IX_NAME_RS_IN term RECEIVE-ALL then metric 0
set policy-options policy-statement IX_NAME_RS_IN term RECEIVE-ALL then local-preference 105
set policy-options policy-statement IX_NAME_RS_IN term RECEIVE-ALL then community set ix-tjb
set policy-options policy-statement IX_NAME_RS_IN term RECEIVE-ALL then community add ix_peer
set policy-options policy-statement IX_NAME_RS_IN term RECEIVE-ALL then accept

set policy-options policy-statement ROUTE_COLLECTOR_IN term REJECT-ALL then reject

set policy-options policy-statement EBGP-EXPORT-TJB term OWN_SUPERNET from community own_aggregate_supernet-tjb
set policy-options policy-statement EBGP-EXPORT-TJB term OWN_SUPERNET then accept
set policy-options policy-statement EBGP-EXPORT-TJB term TRANSIT-CUST-PREFIXES from community transit-cust-with-own-routes
set policy-options policy-statement EBGP-EXPORT-TJB term TRANSIT-CUST-PREFIXES then accept
set policy-options policy-statement EBGP-EXPORT-TJB term MANUAL-PREFIX-LIST from route-filter w.x.y.0/22 exact
set policy-options policy-statement EBGP-EXPORT-TJB term MANUAL-PREFIX-LIST then accept
set policy-options policy-statement EBGP-EXPORT-TJB term REJECT-ALL-ELSE then reject

set policy-options community ix_peer members ASN:nnnnn
set policy-options community transit-cust-with-own-routes members ASN:nnnnn
set policy-options community ix-tjb members ASN:nnnnn
set policy-options community own_aggregate_supernet-tjb members ASN:nnnnn